## Slide 1: 3D Probe Ptychography
Algorithm and preliminary results
Anders F. Pedersen
13-09-2018

## Slide 2: Setup
Sample: ρ
Focused beam (probe): Pj
Optical axis
Objective lens: Aperture: Ap Aberrations: Ab
z
y
x
Slit in image plane: S
Detector (far field)
2θ

## Slide 3: Parameters: Based on 3DBPP
Probe
  2D Gaussian (symmetric)
  Uniform phase (i.e. probe is real)
  Rastered in 2D, perpendicular to the beam direction
Sample
  Complex density
  Phase inspired from edge dislocation wall
  Fixed at central Bragg angle
Objective lens
  CRL, N=70, fN=26.5cm
  Magnification, M=2
  Aperture and aberrations are separated
  Aperture is real 2D symmetric Gaussian
  Aberration is complex with magnitude 1 and variable phase
Slit
  Slit is placed in the image plane
  Slit function is 1 inside slit and 0 outside
  Slit is uniform along x
  Slit is scanned up and down along y

## Slide 4: Algorithm: Based on 3DBPP
Sample plane
Objective plane
Image plane
Detector plane

## Slide 5: Notes on the algorithm
: Fourier transform
: Projection operator, implemented in MatLab as mean(rho,3) along z
: Adjoint projection operator, implemented by repmat(rho,1,1,nz) along z in MatLab
The aperture is not reversed in the back projection, as dividing by the Gaussian is unstable
  Only updating the amplitude weighted by the aperture function with the measured amplitude is unstable
  So currently the amplitude is replaced by the measured amplitude (as is), as shown in the previous slide
Initial guess is typically zeros
  Some amplitude variations may occur where slit positions overlap. This can be suppressed in the algorithm, or it goes away on its own during the reconstruction.
Amplitude variations with a 2-pixel period occurs in the y-direction
  I suppress this by averaging the amplitude in the y-direction every 10 iteration
The lens aberrations seems to be taken into account in the x-direction, but significant blurring is seen in the y-direction

## Slide 6: Reconstruction example
Sample
  Truncated octahedron
  Shape perturbations break symmetry
  Phase is uniform along z
Probe
  RMS width (intensity): 195 nm
  Step size: 172 nm
Slit (dimension relative to sample plane)
  Width: 625 nm
  Step size: 313 nm
3D probe positions
  Only include those with significant intensity
  Total of 1651 3D probe positions
Total 100 iterations
Dose: Maximum pixel intensity 1,000,000

## Slide 7: Reconstruction example: xy-plane (z = 0)
True amplitude
True phase
Reconstructed amplitude
Reconstructed phase

## Slide 8: Reconstruction example: zy-plane (x = 0)
True amplitude
True phase
Reconstructed amplitude
Reconstructed phase

## Slide 9: Reconstruction example: zy-plane (x = 20 px)
True amplitude
True phase
Reconstructed amplitude
Reconstructed phase